## Slide 1: H-1 Modeling & Simulation
November 2025

## Slide 2: Background
ASI presented previous RAM Engineering projects:
  Reliability-Centered Maintenance (RCM) Analysis
  Supportability Optimization Model (SOM)
  Weibull (Life Data) analysis
  Reliability Block Diagrams (RBDs) to predict spares procurements
  Incorporating AI into Data Analytics and Visualization
RAM projects involved numerous types of physical assets:
  Aircraft (Fixed Wing, Helicopters, UAVs)
Ground Vehicles (BFV, FMTV, LVSR)
Facilities (Data centers, Hospitals)
Mining Equipment (Scalers, Elevators, Conveyors)
Other equipment (Engines, Tug Boats, S.E.)
RAM XVII Training Summit

## Slide 3: Background
ASI tasked with utilizing M&S tools and processes to:
  Evaluate various maintenance concepts and compare results
  Evaluate various scenarios and Courses of Action (COAs)
  Incorporate aircraft schedules (Fleet introductions, Depot inductions, Retirements) at the BUNO level
  Incorporate resource allocation and identify excesses and shortages
  Simulate variations in Processes and Turnaround times (TATs) to minimize risk
  Conduct Sensitivity Analyses by altering numerous factors
  Identify the optimal allocation and scheduling/utilization of resources
Models were developed to calculate and predict key metrics:
  Downtime
Wait time
Availability
RBA
Resource utilization
Throughput
Costs
etc.
RAM XVII Training Summit

## Slide 4: Modeling Application
Analysis Tool: Simulation with Arena
Utilizes discrete event simulation capabilities to evaluate current situation as well as alternative solutions
Sensitivity analyses also performed
  Example – Impact of 1 additional Electrician?
  Example – Impact of reducing TAT by 6 days?
  Example – Impact of additional hangar space?
Optimization module identifies “best solution” based on inputs and objectives
Currently used in numerous industries, including DoD services
RAM XVII Training Summit

## Slide 5: Inputs and Outputs
Inputs include:
  All current Aircraft with Delivery, Induction, Preservation, and Retirement schedules
  Future Aircraft
  Maintenance concepts (Intervals, schedules, locations, etc.)
  Depot locations and resources (labor, special equipment, hangar space, etc.)
  Process and TATs for Depot events, ISRs, modifications/changes/upgrades
  Courses of Action (COA) scenarios
  Alternative Maintenance concepts
  Cost information
  Supply chain/logistics information
Outputs included:
  Total Downtime and Wait time
  Aircraft Throughput
  Availability
  Available aircraft (RBA)
  Resource utilization metrics for various COAs
  Cost metrics for various COAs
  Optimal strategies based on desired Availability/Cost
RAM XVII Training Summit

## Slide 6: H-1 IMP Modeling
Objectives
Model Depot inductions, ISRs, and Depot Modifications for UH-1Y and AH-1Z at each site
Identify excess aircraft above RBA requirements to send for preservation
Identify which sites will experience shortfalls/delays, and what additional resources would be required to meet Availability/Readiness requirements
Incorporate predicted ISR occurrences
Run sensitivity analyses on all inputs (ISRs, Depot mods, TATs, resources, etc.)
Identify optimal allocation of resources
Evaluate FH based IMC Concept
Evaluate COAs provided by FST
Run optimization routines on various factors
Status
  Model created with inputs/data from FST
  All BUNOs with locations and induction schedules
  Expected retirement dates calculated/incorporated
  ISRs and Depot modifications incorporated
  FRC Capacities at each site
  Current preservation schedule in effect
RAM XVII Training Summit

## Slide 7: H-1 IMP Modeling – Results
RAM XVII Training Summit
UH-1Y Aircraft Over 10-Year Period
Total UH-1Y
Available UH-1Y
Goal

## Slide 8: H-1 IMP Modeling – Results
Average excess UH-1Y aircraft over PAA and depot requirements
  Minimum of X aircraft and a maximum of X.
  Number varied due to inductions, retirements, WIP, ISRs, MODs, etc.
Depending on maintenance requirements, excess UH-1Y aircraft may be insufficient over 10 year period
Based on the results, an additional Long-Term Preservation policy of X BUNOs was simulated to reduce excess UH-1Y aircraft and approach the baseline inventory.
RAM XVII Training Summit

## Slide 9: H-1 IMP Modeling – Results
RAM XVII Training Summit
UH-1Y Aircraft Over 10-Year Period
Current Plan
Proposed Plan
Goal

## Slide 10: H-1 IMP Modeling - Results
RAM XVII Training Summit
UH-1Y Aircraft Over 10-Year Period (10 Iterations)
Goal

## Slide 11: H-1 IMP Modeling – Results
Considerations for long term preservation scenario
  BUNOs selected for preservation (IMP history, location, flight hours, etc.)
  Additional maintenance requirements due to long term preservation
  Aircraft condition and configuration
RAM XVII Training Summit
Selecting specific BUNOs for preservation allows regulation of IMP schedule
  This offsets IMP to a desirable time frame
  Allows control of which aircraft will compensate for BUNOs in AMARG

## Slide 12: H-1 IMP Modeling - Results
RAM XVII Training Summit

## Slide 13: H-1 IMP Modeling - Demonstration
RAM XVII Training Summit

## Slide 14: H-1 IMP Modeling – Status Update
RAM XVII Training Summit
  Continue to update and validate model against actual induction schedules
  Simulate various COAs for preservation
  Determine impact on fleet inventory
  Vary number of aircraft selected for preservation
  Vary preservation schedule
  Run optimization and sensitivity analyses on various factors to determine impact
  IMP TAT, Depot Mods, increased ISRs, etc.

## Slide 15: H-1 Manpower Study
Model current state (As-Is) operations and predict and evaluate proposed changes of the H-1 maintenance manpower.
Identify opportunities to improve process times and turnaround times associated with current squadron activities.
Run sensitivity analyses and optimization routines to minimize risk associated with implementing proposed changes.
  Utilize Arena OptQuest to Optimize mission capable aircraft while minimizing staffing.
RAM XVII Training Summit

## Slide 16: H-1 Manpower Study – Model Details
Model will run 10 repetitions with a simulation period of 10 years.
Each squadron will be modeled separately to account for differences in shifts, manning, aircraft, and productivity.
Three main work centers will be modeled.
  Airframes
  Avionics
  Flightline
All activities utilizing maintainers will be implemented.
  Maintenance
  Non-MAF duties
  Non-Aeronautical duties
  Administrative tasks
RAM XVII Training Summit

## Slide 17: H-1 Manpower Study – Inputs/Outputs
Inputs:
  Shift schedules
  Current resources and readiness correlation
  Historical and current task turnaround times (FOD Walk, meetings, training, ATAF)
  Historical aircraft downing rate
  Historical maintenance manhour trends
Outputs:
  Mission capable aircraft
  MMH per aircraft
  MMH per Marine by MOS
  Hours spent on non-MAF, non-aeronautical, and administrative tasks.
RAM XVII Training Summit

## Slide 18: H-1 Manpower Study - Constraints
Constraints are centered around staffing, working hours, and duties.
  Staffing and working hours remain consistent throughout the simulation.
The simulation will not extend a Marine’s working hours before or after their assigned shift.
Aircraft assigned to each squadron is fixed throughout the simulation.
  Actual down aircraft are taken into consideration at the beginning of the simulation.
  Based on manpower allocations, aircraft readiness may change.
RAM XVII Training Summit

## Slide 19: H-1 Manpower Study - Results
Availability is considered 11 hours based on the shift length.
  “Workers Mustered” is the average number of workers after Leave and FAPs are accounted for.
  *Total hours include Qual utilization. “Per Marine” does not include Quals.
RAM XVII Training Summit
As-Is Manpower Breakdown per Day per Marine
NUMBERS DO NOT REFLECT ACTUAL DATA

## Slide 20: H-1 Manpower Study - Results
RAM XVII Training Summit
Mission Capable Aircraft % (PAA)
NUMBERS DO NOT REFLECT ACTUAL DATA

## Slide 21: H-1 Manpower Study - Results
Average mission capable aircraft: 65.0%
It takes an average of 50.0 DMMH to bring an aircraft from “down” to “up” status.
  After disregarding the top and bottom 25% of values (removing outliers), the average equates to 13.0 DMMH.
  Average of 300 DMMH on down aircraft over 30 days.
  Average of 700 DMMH on down aircraft over 180 days.
30.0% of a Marine’s time is spent on direct maintenance.
  40.0% of total DMMH are spent working on down aircraft.
45.0% of a Marine’s time is spent on productive non-recorded activities.
  41.0% of that time is in support of D/T’s, Fueling, Launch and Recovery, Towing, and Troubleshooting.
  36.0% encompasses FOD Walks, end of shift cleanup and Field Day.
  23.0% includes admin activities, tech training and meetings.
RAM XVII Training Summit
NUMBERS DO NOT REFLECT ACTUAL DATA

## Slide 22: H-1 Manpower Study - Proposal
Mission capability goal: 75%
Two courses of action to increase MMH and decrease down aircraft turnaround time.
  Increase maintenance productivity.
  Increase staffing
    FAPs/SAPs may also be reallocated among the work centers instead of overall increases.
It is assumed that productive activities not recorded on a MAF are required in support of the fleet and will not be adjusted.
  The amount of time during a shift that a Marine has available to complete maintenance will stay the same.
RAM XVII Training Summit

## Slide 23: H-1 Manpower Study – FAP/SAPs
RAM XVII Training Summit
Muster/ASR Gap
  Difference between available workers (510) and recorded On-Hand (1155) for CPL and below is 645 (CDI/CDQARs, SAPs and FAPs).
  Difference between average daily muster (480) and available workers (510) is attributed to Leave (30).
  Data collected between Jun ‘18 and Mar ’19.
NUMBERS DO NOT REFLECT ACTUAL DATA

## Slide 24: H-1 Manpower Study – Proposal Results
RAM XVII Training Summit
Various Manpower Breakdowns per Day per Marine
Availability is considered 11 hours based on the shift length.
  Non-MAF tasks include D/T, Fueling, Launch and Recovery, Towing, and Troubleshooting.
  Non-Aeronautical tasks include FOD Walk, ATAF, and Field Day.
  Administrative tasks include Tech Training, Greenside Training, and Meetings.
  Unaccounted Time includes all breaks, lunch, and irregular events (i.e. medical, missing tool search, travel to/from work centers, etc.).
Goal 1: +10 AF, +30 AVI, +10 FL. Goal 2: +20 AF, +30 AVI, +20 FL.
Without a change in current processes and policies,
inefficiencies will increase with added Marines.
NUMBERS DO NOT REFLECT ACTUAL DATA

## Slide 25: H-1 Manpower Study
RAM XVII Training Summit
Mission Capable Aircraft %
NUMBERS DO NOT REFLECT ACTUAL DATA

## Slide 26: H-1 Manpower Study
RAM XVII Training Summit
Various Manpower Breakdowns per Day per Marine
Availability is considered 11 hours based on the shift length.
  Non-MAF tasks include D/T, Fueling, Launch and Recovery, Towing, and Troubleshooting.
  Non-Aeronautical tasks include FOD Walk, ATAF, and Field Day.
  Administrative tasks include Tech Training, Greenside Training, and Meetings.
  Unaccounted Time includes all breaks, lunch, and irregular events (i.e. medical, missing tool search, travel to/from work centers, etc.).
*All Quals (SSGT and below) were utilized for maintenance 20% of the allotted maintenance time.
**Quals were not considered in the total Marine count when
determining hours “per Marine.”
NUMBERS DO NOT REFLECT ACTUAL DATA

## Slide 27: H-1 Manpower Study - OptQuest
Arena OptQuest searches for the most optimal solutions within a model when given controls, constraints, and objectives.
The quantity of workers for each shift and work center was optimized while maximizing mission capability and remaining within overall worker quantity.
100 simulations with 10 repetitions each were run for each scenario. Only one squadron was analyzed.
RAM XVII Training Summit

## Slide 28: H-1 Manpower Study - OptQuest
RAM XVII Training Summit
Best Solutions Based on Current Staffing on 1 Squadron*
Mission Capability
*Current total worker quantity: 53 E1-E3
NUMBERS DO NOT REFLECT ACTUAL DATA

## Slide 29: H-1 Manpower Study - OptQuest
RAM XVII Training Summit
 | Airframes | Avionics | Flightline
Day | 9 | 8 | 7, PC: 4
Night | 8 | 7 | 6, PC: 4
 | Airframes | Avionics | Flightline
Day | 11 | 8 | 11, PC: 4
Night | 7 | 4 | 5, PC: 3
Current
Best Solution
Highest average Mission Capability: 68.1%
  11.0% increase from current maintainer placement.
  Though Avionics has more Total MMH per Marine, Airframes and Flightline have a historically higher ratio of Down Aircraft MMH to Total MMH.
NUMBERS DO NOT REFLECT ACTUAL DATA

## Slide 30: H-1 Manpower Study - OptQuest
RAM XVII Training Summit
Best Solution Based on T/O (78 E1-E3)
Mission capability increase: 3%
Best Solution Based on ASR (72 E1-E3)
Mission capability increase: 5.1%
Shift | Airframes | Avionics | Flightline
Day | 15 | 12 | 8, PC: 5
Night | 15 | 11 | 7, PC: 5
Shift | Airframes | Avionics | Flightline
Day | 18 | 16 | 13, PC: 5
Night | 8 | 5 | 5, PC: 8
Current (76.6% MC)
Best Solution (80.6% MC)
Shift | Airframes | Avionics | Flightline
Day | 14 | 11 | 7, PC: 5
Night | 14 | 10 | 6, PC: 5
Shift | Airframes | Avionics | Flightline
Day | 15 | 13 | 12, PC: 4
Night | 7 | 7 | 4, PC: 8
Current (73.5% MC)
Best Solution (78.6% MC)
NUMBERS DO NOT REFLECT ACTUAL DATA

## Slide 31
Questions???
RAM XV Training Summit