## Slide 1: Missions To and Around the Moon How Historical Failures Provide Context for Present Decisions
Elise Doan, NASA Marshall Space Flight Center
Frank Hark, Bastion Technologies
Intro
Tries
Fails
Cases
Outro
This publication does not contain information which falls under the purview of the U.S. Munitions List (USML), as defined in the International Traffic in Arms Regulations (ITAR), 22 CFR 120-130, nor the Export Administration Regulation (EAR), 15 CFR 730-774, and is not export controlled.

## Slide 2: Scope
All missions to or around the moon from Pioneer 0 in Aug 1958 to Lunar Trailblazer in Feb 2025 (142 over 66.5 years).
  Who – Which countries and companies built and operated these missions?
  What – What was the mass of the spacecraft and what came before?
  Where – Where was the mission intended to go?
  When – When did the mission launch, reach orbit, land, collect samples, return, end and/or fail?
  Why – What was the mission objective? What was the failure mode?
  How – Did they succeed or fail?
Intro
Tries
Fails
Cases
Outro

## Slide 3: Attempts
Chart: Missions by Country
| America | USSR | Russia | China | Other
 | 60 | 53 | 4 | 10 | 15
Missions were categorized by their furthest objective.
It is assumed that the farther a mission goes, the more complicated it is.
More complicated missions are assumed to encompass the objectives of less complicated missions.
(e.g. To land, a mission must reach lunar orbit, and to reach lunar orbit, the spacecraft must fly near the moon.)
142 Total Missions. 9 Crewed = 6% (Apollo)
Chart: Missions by Ambition
| 1 | 2 | 3 | 4 | 5 | 6
Missions | 25 | 51 | 10 | 26 | 11 | 19
Intro
Tries
Fails
Cases
Outro

## Slide 4
Chart: Mission Type Attempts by Country
| America | USSR | Russia | China | Other
1 | 9 | 10 | 2 | 0 | 4
2 | 26 | 13 | 1 | 6 | 5
3 | 4 | 6 | 0 | 0 | 0
4 | 12 | 10 | 1 | 0 | 3
5 | 2 | 4 | 0 | 2 | 3
6 | 7 | 10 | 0 | 2 | 0
Flyby
Orbit
Impact
Land
Rove
Return
Intro
Tries
Fails
Cases
Outro

## Slide 5
Apollo
Zond
Luna
Ranger,
Lunar Orbiter
’78-’90
HLS Announced
First Independent
Commercial Attempt
50% failed
’76-’13
Intro
Tries
Fails
Cases
Outro
36%Failed 45%Failed 60%Failed 65%Failed 73%Failed 42%Failed
(9/25) (23/51) (6/10) (17/26) (8/11) (8/19)
Notes: Put %failed for each ambition

## Slide 6
HLS Announced
First Independent Commercial Attempt
28 Missions since 2012
46% Failed (15/28)
Intro
Tries
Fails
Cases
Outro

## Slide 7
Apollo
Zond
Luna
Ranger,
Lunar Orbiter
’78-’90
HLS Announced
First Independent
Commercial Attempt
’76-’13
Intro
Tries
Fails
Cases
Outro

## Slide 8
HLS Announced
First Independent Commercial Attempt
Intro
Tries
Fails
Cases
Outro

## Slide 9
Chart: Landing Sites
| 209.94766999999999 | 126.27302 | 77 | -87.1 | -4 | 12.9 | 179.2 | 53.27 | 82.8
Artemis III | -89.5343 | -89.017 | -87.3 | -88.5 | -86.9 | -84.9 | -38.3 | -85.28 | -84.5
LandFail | -15.5 | 9.1 | 9.8 | 8 | -4 | 0.45 | -80.13 | 32.5956 | 60.5 | -57.865
RoveFail | -70.881 | -84.7906 | 25.85 | 47.581
ReturnFail | 3.34 | 17 | 12.6669
Apollo | -3.0124 | -3.6453 | 26.1322 | -8.973 | 0.67416 | 20.1908
ImpactSucc | -10.634 | -12.83 | 29.1 | 2.6377
LandSucc | 7.1 | 18.87 | -2.474 | -3.0161 | -41.01 | 0.46 | 1.41 | -13.316 | -69.373 | 18.56
RoveSucc | 38.28 | -45.444
ReturnSucc | -41.6385 | 43.0576 | -0.5137 | 3.7863 | 12.7145
59% Failed (39/66)
Intro
Tries
Fails
Cases
Outro

## Slide 10
Chart: Failure Rate Estimate by Mission Ambition
| Flyby | Orbit | Impact | Land | Rove | Return
Min | 0.06338 | 0.19658 | 0.090909 | 0.30357 | 0.26667 | 0.42105
Low | 0.22373 | 0.32295 | 0.28983 | 0.48714 | 0.42445 | 0.33876
Mean | 0.26056 | 0.36752 | 0.34848 | 0.55357 | 0.51724 | 0.45
High | 0.2974 | 0.41209 | 0.40714 | 0.62 | 0.61003 | 0.56124
Max | 0.36 | 0.45098 | 0.6 | 0.65385 | 0.72727 | 0.42105
Flyby Orbit Impact Land Rove Return
These are conservative extrapolations, only based on demonstrated capability. They do not account for Reliability Growth.
Flyby
Orbit
Impact
Land
Rove
Return
Intro
Tries
Fails
Cases
Outro
Chart: % Failed by Ambition
| 1 | 2 | 3 | 4 | 5 | 6
Independent | 0.36 | 0.45098 | 0.6 | 0.65385 | 0.72727 | 0.42105
Cummulative | 0.06338 | 0.19658 | 0.090909 | 0.30357 | 0.26667 | 0.42105

## Slide 11
Intro
Tries
Fails
Cases
Outro
Chart: % Failed Over Time

## Slide 12
Intro
Tries
Fails
Cases
Outro
Chart: % Failed Over Time
| 41524.143750000003 | 41609.729166666664 | 41935.75 | 43208 | 43241 | 43441 | 43518.072916666664 | 43668.384166666663 | 44158.854305555556 | 44740 | 44777.964444444442 | 44881 | 44906.318055555559 | 45030.510138888887 | 45121.378668981481 | 45148 | 45175.987627314818 | 45299.304606481484 | 45336 | 45364 | 45371.021851851852 | 45415 | 45672.258090277777 | 45672.258090277777 | 45715 | 45715 | 45715.011458333334 | 45715.011458333334
Overall | 0 | 0.5 | 0.33333 | 0.25 | 0.4 | 0.33333 | 0.42857 | 0.5 | 0.44444 | 0.4 | 0.36364 | 0.33333 | 0.38462 | 0.35714 | 0.33333 | 0.375 | 0.35294 | 0.38889 | 0.42105 | 0.45 | 0.42857 | 0.40909 | 0.43478 | 0.41667 | 0.44 | 0.46154 | 0.48148 | 0.5
Flyby | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.055556 | 0.052632 | 0.05 | 0.047619 | 0.045455 | 0.043478 | 0.041667 | 0.08 | 0.11538 | 0.11111 | 0.10714
Orbit | 0 | 0 | 0 | 0 | 0.25 | 0.2 | 0.16667 | 0.14286 | 0.125 | 0.11111 | 0.1 | 0.090909 | 0.083333 | 0.083333 | 0.076923 | 0.071429 | 0.066667 | 0.125 | 0.11765 | 0.16667 | 0.15789 | 0.15 | 0.14286 | 0.13636 | 0.13636 | 0.17391 | 0.20833 | 0.2
Impact | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.1 | 0.090909 | 0.090909 | 0.090909 | 0.083333 | 0.076923 | 0.071429 | 0.071429 | 0.071429 | 0.071429 | 0.066667
Land | 0 | 0 | 0 | 0 | 0 | 0.33333 | 0.5 | 0.4 | 0.4 | 0.4 | 0.4 | 0.5 | 0.5 | 0.42857 | 0.5 | 0.44444 | 0.5 | 0.54545 | 0.54545 | 0.54545 | 0.5 | 0.53846 | 0.5 | 0.5 | 0.5 | 0.5 | 0.53333
Rove | 1 | 1 | 1 | 1 | 0.5 | 0.5 | 0.66667 | 0.5 | 0.5 | 0.5 | 0.5 | 0.6 | 0.6 | 0.5 | 0.5 | 0.5 | 0.57143 | 0.57143 | 0.57143 | 0.57143 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.55556
AveragePerc | 0 | 0.1 | 0.066667 | 0.05 | 0.14 | 0.11667 | 0.13571 | 0.16875 | 0.15 | 0.135 | 0.12273 | 0.1125 | 0.13462 | 0.125 | 0.11667 | 0.125 | 0.11765 | 0.16667 | 0.17105 | 0.1875 | 0.17857 | 0.17045 | 0.17391 | 0.16667 | 0.2 | 0.23077 | 0.24074 | 0.24643

## Slide 13
Flyby
Orbit
Impact
Land
Rove
Return
Intro
Tries
Fails
Cases
Outro
Chart: % Failed by Type and Country
| America | USSR | Russia | China | Other
1 | 0.33333 | 0.6 | 0 | 0 | 0
2 | 0.38462 | 0.61538 | 1 | 0.33333 | 0.4
3 | 0.25 | 0.83333 | 0 | 0 | 0
4 | 0.5 | 0.8 | 1 | 0 | 0.66667
5 | 1 | 0.75 | 0 | 0.5 | 0.66667
6 | 0.14286 | 0.7 | 0 | 0 | 0
Chart: % Failed by Country
| America | USSR | Russia | China | Other
Rate | 0.38333 | 0.69811 | 0.5 | 0.3 | 0.4

## Slide 14: What Went Wrong?
Total Non-Launch Failures: 40, 57% of 70 Total Failures
Launch, EPS, and GNC failures are more likely to end a mission earlier.
Mechanical, propulsion, and communication failures are more likely to end a mission at a later stage.
Intro
Tries
Fails
Cases
Outro
Chart: Failure Modes
| GNC | Communication | Power | Mechanical | Propulsion
 | 17 | 7 | 4 | 5 | 7

## Slide 15
Flyby
Orbit
Impact
Land
Rove
Return
Intro
Tries
Fails
Cases
Outro
Chart: Failure Modes by Phase
| 0 | 1 | 2 | 3 | 4 | 5
Communication | 2 | 3 | 0 | 2 | 0 | 0
EPS | 2 | 0 | 2 | 0 | 0 | 0
GNC | 2 | 5 | 0 | 9 | 1 | 0
MECH | 1 | 2 | 0 | 1 | 1 | 0
Propulsion | 1 | 4 | 1 | 1 | 0 | 0
9 GNC Failures During Landing
6 in the last decade
4 traced to lunar environment interfering with altimeters and range-finders, both radar and laser
(Others due to failed IMU, and/or software incorrectly commanding main engines in response to GNC sensor data)
Notes: Label and explain GNC in landing

## Slide 16
Intro
Tries
Fails
Cases
Outro

## Slide 17
Intro
Tries
Fails
Cases
Outro

## Slide 18: Notable Cases
Hakuto-R Mission 1: Communication lost during landing descent
Beresheet: Gyroscopes failed, triggering main engine shut off and crash landing
IM-2: Communication lost during landing, sideways when re-connected, thus power lost
Apollo/Artemis Con-ops comparison
Intro
Tries
Fails
Cases
Outro

## Slide 19: Hakuto-R Mission 1
Mission Objective: Rove
Started as a Google Lunar-X Prize project
Dec 22 Falcon 9 launch
Slow long travel to conserve fuel
Unreliable telemetry identified incorrect landing site
Communication lost during descent
Lander was hovering 5km above surface because the flight computer software assumed radar data was faulty
Crashed when propellant ran out
Intro
Tries
Fails
Cases
Outro

## Slide 20: Beresheet
Mission Objective: Land
Google Lunar X Prize
Feb 2019 Falcon 9 Launch
Inspired/became Blue Ghost (Firefly)
During braking Gyroscopes failed leading to main engine shut off
Sudden loss of communication meant that the ground team could not reset the component
Comm regained too late to slow descent (500km/hr 150m above the surface)
Intro
Tries
Fails
Cases
Outro

## Slide 21: IM-2
Mission Objective: Rove
CLPS Program
Feb 25 Falcon 9 Launch
During descent, dust obscured laser and range, and radio comm.
After landing, low power and a broken antenna indicated it was on its side (imagery confirmed)
Altimeter failing caused computer to steer into a plateau edge.
Crash also coated solar panels in dust.
Intro
Tries
Fails
Cases
Outro

## Slide 22: Apollo LEM vs Artemis HLS
Apollo Landings 1969-1972
Artemis III Con-ops
Intro
Tries
Fails
Cases
Outro
Notes: Crew module in different orbit, will that affect comm relays?
Can crew control mitigate the reliance on impacted sensors?

## Slide 23: Summary
Landing is a high-risk phase of moon missions
Primarily due to plume interactions that interfere with telemetry and communications
Loss of communication should be expected, creating increased reliance on sensor readings during landing
American Industry is re-learning how to do this after decades-long break, leading to a gap in knowledge
Intro
Tries
Fails
Cases
Outro

## Slide 24: Missions to and Around Mars
By Elise Doan/ES61
For Frank Hark/QD35
Intro
Tries
Fails
Outro
This publication does not contain information which falls under the purview of the U.S. Munitions List (USML), as defined in the International Traffic in Arms Regulations (ITAR), 22 CFR 120-130, nor the Export Administration Regulation (EAR), 15 CFR 730-774, and is not export controlled.

## Slide 25: Scope
All missions to or around Mars from Mars 1M No.1 in Oct. 1960 to Europa Clipper in Oct. 2024 (52 over 64 years).
  Who – Which countries and companies built and operated these missions?
  What – What was the mass of the spacecraft?
  Where – Where was the mission intended to go?
  When – When did the mission launch, reach orbit, land, collect data, end and/or fail?
  Why – What was the mission objective? What was the failure mode?
  How – Did they succeed or fail?
Intro
Tries
Fails
Outro

## Slide 26: Attempts
Chart: Missions By Country
| America | USSR | Russia | China
Missions | 25 | 17 | 2 | 1
Chart: Missions by Ambition
| 1 | 2 | 3 | 4
 | 13 | 16 | 13 | 9
Missions were categorized by their furthest objective.
It is assumed that the farther a mission goes, the more complicated it is.
More complicated missions are assumed to encompass the objectives of less complicated missions.
(e.g. To land, a mission must reach lunar orbit, and to reach lunar orbit, the spacecraft must fly near the moon.)
52 Total Missions
Intro
Tries
Fails
Outro

## Slide 27
Chart: Mission Attempts by Country and Ambition
| 1 | 2 | 3 | 4
America | 6 | 8 | 5 | 5
USSR | 5 | 5 | 5 | 2
Russia | 0 | 0 | 1 | 1
China | 0 | 0 | 0 | 1
Flyby
Orbit
Land
Rove
Intro
Tries
Fails
Outro

## Slide 28
Intro
Tries
Fails
Outro
Notes: Missions have generally gotten more complex and successful over time

## Slide 29
Intro
Tries
Fails
Outro

## Slide 30
Chart: Landing Sites
| -195 | -19.420000000000002 | -24.550000000000011
LandFail | -76 | -23.9 | 18.2
LandSucc | 47.64 | 68.2188 | 4.5024 | 22.27
RoveFail | -45 | -45.0445
RoveSucc | 19.748 | 18.4447 | 25.066 | -4.5895 | -14.5684 | -1.9462
Intro
Tries
Fails
Outro
Notes: We have had more success in the northern hemisphere of the planet than the southern (orbital tilt?)

## Slide 31
Chart: % Failed by Ambition
Independent | 0.46154 | 0.5 | 0.69231 | 0.33333
Cummulative | 0.11765 | 0.21053 | 0.40909 | 0.33333
Flyby
Orbit
Land
Rove
Chart: Estimated Failure Rate
Min | 0.11765 | 0.21053 | 0.40909 | 0.33333
Low | 0.23031 | 0.24038 | 0.4393 | 0.1762
Mean | 0.29412 | 0.31579 | 0.54545 | 0.33333
High | 0.35792 | 0.39119 | 0.65161 | 0.49047
Max | 0.46154 | 0.5 | 0.69231 | 0.33333
These are conservative extrapolations, only based on demonstrated capability. They do not account for Reliability Growth.
Intro
Tries
Fails
Outro
Notes: Landing is still the highest risk phase of a Mars mission, despite extended duration of flybys and added complexity of roving.

## Slide 32
Chart: %Failed Over Time
| 22199.602650462963 | 22203.577118055557 | 22943.746585648147 | 22951.676388888889 | 22954.649479166666 | 23686.807002314814 | 23709.598622685186 | 23711.55 | 25259.061828703703 | 25289.444965277777 | 25289.931944444445 | 25295.439583333333 | 26062.049328703702 | 26063.707430555554 | 26072.682453703703 | 26081.64340277778 | 26083.932685185184 | 26866.81318287037 | 26870.78875 | 26881.74013888889 | 26885.708530092594 | 27626.890277777777 | 27646.777083333334 | 32331.73476851852 | 32336.709525462964 | 33872.711817129632 | 35376.708333333336 | 35385.867280092592 | 35403.290358796294 | 35979.758333333331 | 36140.781840277778 | 36163.848032407404 | 36988.626643518517 | 37774.739583333336 | 37782.749155092592 | 37810.137499999997 | 38048.304062499999 | 38576.488194444442 | 39298.393055555556 | 39352.481944444444 | 40855.844467592593 | 40873.626400462963 | 41583.380555555559 | 41596.769444444442 | 42443.396527777775 | 43225.461817129632 | 44032.915439814817 | 44035.1953125 | 44042.493055555555 | 45212.59652777778 | 45572.619571759256 | 45579.67083333333
Overall | 1 | 1 | 1 | 1 | 1 | 1 | 0.85714 | 0.875 | 0.77778 | 0.8 | 0.72727 | 0.75 | 0.76923 | 0.78571 | 0.8 | 0.8125 | 0.76471 | 0.77778 | 0.73684 | 0.75 | 0.7619 | 0.72727 | 0.69565 | 0.70833 | 0.72 | 0.73077 | 0.7037 | 0.71429 | 0.68966 | 0.7 | 0.70968 | 0.71875 | 0.69697 | 0.70588 | 0.68571 | 0.66667 | 0.64865 | 0.63158 | 0.61538 | 0.6 | 0.60976 | 0.59524 | 0.5814 | 0.56818 | 0.57778 | 0.56522 | 0.55319 | 0.54167 | 0.53061 | 0.52 | 0.5098 | 0.5
Flyby | 1 | 1 | 1 | 1 | 1 | 1 | 0.85714 | 0.875 | 0.77778 | 0.8 | 0.72727 | 0.75 | 0.76923 | 0.78571 | 0.73333 | 0.6875 | 0.64706 | 0.61111 | 0.57895 | 0.55 | 0.52381 | 0.5 | 0.47826 | 0.5 | 0.48 | 0.5 | 0.48148 | 0.5 | 0.48276 | 0.46667 | 0.45161 | 0.4375 | 0.42424 | 0.41176 | 0.4 | 0.38889 | 0.37838 | 0.36842 | 0.35897 | 0.35 | 0.36585 | 0.35714 | 0.34884 | 0.34091 | 0.33333 | 0.32609 | 0.31915 | 0.3125 | 0.30612 | 0.30612 | 0.3 | 0.29412
Orbit | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.83333 | 0.71429 | 0.625 | 0.66667 | 0.6 | 0.54545 | 0.5 | 0.46154 | 0.42857 | 0.46667 | 0.4375 | 0.47059 | 0.44444 | 0.47368 | 0.45 | 0.47619 | 0.5 | 0.47826 | 0.45833 | 0.44 | 0.42308 | 0.40741 | 0.40741 | 0.39286 | 0.37931 | 0.37931 | 0.4 | 0.3871 | 0.375 | 0.36364 | 0.35294 | 0.34286 | 0.33333 | 0.32432 | 0.31579 | 0.31579 | 0.31579 | 0.31579
Land | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.83333 | 0.71429 | 0.75 | 0.77778 | 0.77778 | 0.77778 | 0.8 | 0.72727 | 0.72727 | 0.72727 | 0.75 | 0.75 | 0.76923 | 0.71429 | 0.66667 | 0.66667 | 0.66667 | 0.625 | 0.625 | 0.64706 | 0.61111 | 0.61111 | 0.61111 | 0.63158 | 0.6 | 0.6 | 0.57143 | 0.54545 | 0.54545 | 0.54545 | 0.54545
Rove | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.66667 | 0.66667 | 0.66667 | 0.66667 | 0.66667 | 0.66667 | 0.5 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.5 | 0.42857 | 0.42857 | 0.42857 | 0.42857 | 0.42857 | 0.42857 | 0.375 | 0.33333 | 0.33333 | 0.33333 | 0.33333
AveragePerc | 1 | 1 | 1 | 1 | 1 | 1 | 0.85714 | 0.875 | 0.77778 | 0.8 | 0.72727 | 0.75 | 0.76923 | 0.78571 | 0.76667 | 0.75 | 0.70588 | 0.69444 | 0.65789 | 0.64167 | 0.62698 | 0.59848 | 0.57246 | 0.59028 | 0.58 | 0.59615 | 0.57407 | 0.58929 | 0.56897 | 0.56667 | 0.56452 | 0.55729 | 0.5404 | 0.53431 | 0.51905 | 0.50463 | 0.49099 | 0.47807 | 0.46581 | 0.45417 | 0.46748 | 0.45635 | 0.44574 | 0.43561 | 0.43333 | 0.42391 | 0.41489 | 0.40625 | 0.39796 | 0.39796 | 0.39 | 0.38235
Intro
Tries
Fails
Outro
Notes: We see expected learning and reliability growth, with landing being consistently more risky than the overall, average, or other mission phases

## Slide 33
Chart: % Failed by Country and Ambition
| Flyby | Orbit | Land | Rove
America | 0.16667 | 0.375 | 0.2 | 0
USSR | 1 | 0.8 | 1 | 1
Russia | 0 | 0 | 1 | 1
China | 0 | 0 | 0 | 0
Chart: % Failed By Country
| America | USSR | Russia | China
Rate | 0.2 | 0.94118 | 1 | 0
Intro
Tries
Fails
Outro
Notes: The USSR had nearly ubiquitous failures, most of them due to launch vehicles. Most of America’s failures have been on orbiter missions, with incredible success in rover missions. (Props to JPL).

## Slide 34: What Went Wrong?
Chart: Common Failure Modes
| Crash | Launch | Power | Software | Propulsion | Computer | Environment | Communication
 | 1 | 10 | 3 | 2 | 4 | 4 | 1 | 1
Intro
Tries
Fails
Outro
Notes: Different than missions to the moon, computer radiation hardening seems to be a bigger challenge for Mars missions. Additionally, propulsion systems must be more robust during long distances.

## Slide 35
Chart: Failure Modes by Phase
| Crash | Launch | Power | Software | Propulsion | Computer | Environment | Communication
0 | 0 | 10 | 2 | 0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0
2 | 1 | 0 | 1 | 1 | 2 | 2 | 1 | 0
3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Flyby
Orbit
Land
Rove
Intro
Tries
Fails
Outro

## Slide 36
Intro
Tries
Fails
Outro
Notes: Generally less launch failures over time

## Slide 37: Summary
We see an expected amount of reliability growth, learning, and knowledge transfer from a more consistent cadence of Mars missions.
Landing is still the highest risk mission phase.
America is highly successful and remarkably dominant in this arena of space exploration (JPL led).
Intro
Tries
Fails
Outro